Vertex: a basic class to represent a single vertex/node in a graph

Fields:

long int distanceFromInitial: a long integer used in memoizing a graph to build a minimum spanning tree (MST); it is the distance of the shortest path known from some initial node (or LONG_MAX if this Vertex has not yet been memoized)

vector<Vertex*> pathFromInitial: an ordered record of the nodes encountered along the shortest known path from some initial node (with a number of elements equal to distanceFromInitial+1)

vector <Vertex*> neighbors: a set of the neighbors to which this Vertex is connected

long int startTime: a protected field recording the time of this Vertex's creation; should not be accessed directly

Methods:

Vertex() or Vertex(long int startTime): may be either empty or initialized with the time of this Vertex's creation

void addNeighbor(Vertex* neighbor): adds a pointer to another Vertex to this Vertex's set of neighbors, and adds this Vertex to the other Vertex's neighbors

double clusteringCoefficient(): calculates the clustering coefficient (# of links between neighbors / # of possible links between neighbors) of this Vertex

long int getStartTime(): getter method for startTime, as it should not be accessed directly

bool hasNeighbor(Vertex* neighbor): checks that a pointer to Vertex is actually a neighbor of this Vertex

Graph: a basic collection of Vertices

Fields:

vector<Vertex*> nodes: a set of the nodes contained in this Graph

Methods:

void addNode(Vertex* node): adds a Vertex to the set of nodes

double averagePathLength(): determines the mean length of the shortest path between any two nodes, averaged across all pairs of nodes, by building a MST for each node

long int nodesWithDegree(long int k): returns the number of nodes with degree k

double* degreeDistribution(): returns a dynamically allocated array relating the degree of a node (the index) to the proportion of nodes in the graph with that degree (the element); since the theoretical maximum degree is the same as the number of nodes minus one, the size of the array is the same as the number of nodes in the Graph

double averageDegree(): calculates and returns the average (not necessarily integer) degree of the nodes in the Graph

double averageClusteringCoefficient(): calculates and returns the mean clustering coefficient of the nodes in the Graph using the method Vertex::clusteringCoefficient()

void insertNode(Vertex* node, long int position): inserts a node at the specified position such that every element in that position and further is moved up by one index

long int indexOf(Vertex* node): finds the index in Graph::nodes of the given Vertex*

void memoize(Vertex* root): simpler method to set up the start of memoization using Graph::memoize(Vertex* root, vector<Vertex*> path, long int distance)

void memoize(Vertex* root, vector<Vertex*> path, long int distance): an unweighted implementation of Djikstra's algorithm, lacking a top-level MST in favor of storing shortest path information in the nodes themselves in Vertex::pathFromInitial and Vertex::distanceFromInitial

void clean(Vertex* root): a recursive method to go through and remove all memoization from the nodes of the graph, setting Vertex::distanceFromInitial to LONG_MAX and emptying pathFromInitial of its contents

GrowingNetwork: an abstract derived class of Graph which incorporates the concepts of time and growth as according to the growing network model put forth by Ozik, Hunt, and Ott in Physical Review E (2004)

Fields:

long int m: the growth parameter; whenever a new node is added, it forms edges with the m closest nodes

long int time: the GrowingNetwork's current time, used to set Vertex::startTime on node creation; this field should not be accessed directly, and instead should be accessed with the methods GrowingNetwork::getTime() and GrowingNetwork::tick()

Methods:

long int getTime(): getter method for the time field, which should not be directly accessed

void tick(): increments the current time, which should not be directly accessed

void grow(long int n): virtual method to grow n new nodes in the graph; implementation will depend on the geometry of the implementing derived class

long int edgeAge(Vertex* a, Vertex* b): calculates the time difference between the current time and the time at which the edge between a and b was added; returns -1 if no such edge exists

double* edgeAgeVsConnectivity(): returns a dynamically allocated array relating the age of an edge (the index) to its average connectivity/between-ness/shortcutness (the element), defined as the proportion of shortest paths between pairs of nodes of which it is a part; since the maximum age is the number of nodes minus one, the size of the array is the same as the number of nodes in the GrowingNetwork

GrowingNetwork2D: an implementation of a growing network in two dimensions such that all nodes are equally spaced on a circle, derived from the abstract class GrowingNetwork; note that this implementation does not simulate actual position, but rather uses indices in the GrowingNetwork2D::nodes field as equally-spaced intervals

Fields: no new fields

Methods:

GrowingNetwork2D(long int n, long int m): a constructor which begins by placing m+1 nodes in a clique, then growing the remaining n – (m+1) nodes using GrowingNetwork2D::grow(long int n) with parameter n = n - (m+1)

void grow(long int n): grows n additional nodes onto the graph using the following algorithm (requires an even value of m):
            1. select, from a uniform distribution, a random index between zero and the number of nodes in the graph minus one
            2. create a new node and insert it at index + 1 using Graph::insertNode(Vertex* node)
            3. add edges from the new node to the m/2 nodes before and the m/2 nodes after index + 1
            4. repeat until n nodes have been added

long int edgeArcDistance(Vertex* a, Vertex* b): gives the distance between two Vertices along the arc of the circle on which all nodes lie (in units of inter-node intervals along the circle), but does not check that an edge between them actually exists

double* edgeAgeVsArcDistance(): returns a dynamically allocated array relating the age of an edge (the index) to its average arc distance (the element) as defined by the method GrowingNetwork2D::edgeArcDistance(Vertex* a, Vertex* b); since the maximum age is the number of nodes minus one, the size of the array is the same as the number of nodes in the GrowingNetwork

double edgeLinearDistance(Vertex* a, Vertex* b): gives the linear distance between two Vertices along the length of the edge, using the return value from GrowingNetwork2D::edgeArcDistance(Vertex* a, Vertex* b) to calculate the length of the corresponding chord

double* edgeAgeVsLinearDistance: returns a dynamically allocated array relating the age of an edge (the index) to its average linear distance (the element) as defined by the method GrowingNetwork2D::edgeLinearDistance(Vertex* a, Vertex* b); since the maximum age is the number of nodes minus one, the size of the array is the same as the number of nodes in the GrowingNetwork

double* edgeArcDistanceDistribution: returns a dynamically allocated array relating the degree of a arc distance of an edge (the index) to the proportion of edges in the GrowingNetwork with that arc distance (the element); since the maximum age is the number of nodes minus one, the array's size is equal to the number of nodes in the GrowingNetwork

SpatialVertex: a class derived from Vertex which incorporates a position in an arbitray number of dimensions, in an arbitrary coordinate system; it is the responsibility of container classes to impose a common coordinate system and define operations on those coordinates

Fields:

dimension: a record of the dimension of this SpatialVertex; two SpatialVertices with different dimensions cannot be meaningfully compared

position: an array of floating-point values of length equal to the dimension, storing the components of the position of this SpatialVertex

Methods:

SpatialVertex(long int dimension, double* position, long int startTime): must be initialized with a dimension, position array, and starting time

long int getDimension(): getter method for accessing the dimension, which is protected

double getPosition(): getter method for accessing the position, which is protected

~SpatialVertex(): this overridden destructor also deletes the position array, which must be dynamically allocated in order to handle arbitrary dimensions

GrowingNetwork3D: an implementation of a GrowingNetwork such that all nodes are placed on the surface of a sphere, using SpatialVertices and an equalization algorithm to approximate even spacing

Fields:

vector<SpatialVertex*> nodes: the set of nodes in this graph, each with a position on the sphere in spherical coordinates (with the implicit, irrelevant radial component omitted), giving them a dimension of three but only two position values

Methods:

GrowingNetwork3D(long int n, long int m): arranges the first m+1 nodes in a clique on the sphere in an equalized configuration, then grows the remaining n – (m+1) nodes using GrowingNetwork3D::grow(long int n) with n – (m+1) as the parameter n

grow(long int n): grows n additional nodes onto the graph using the following algorithm:
1. choose a random location on the sphere using the method GrowingNetwork3D::randomLocation()
2. place a new SpatialVertex there and connect it to its m nearest neighbors, obtained from the method GrowingNetwork3D::findMNearestNeighbors(SpatialVertex* start)
3. run GrowingNetwork3D::equalize() to attempt to evenly space the nodes across the surface of the sphere (approximately)
4. repeat until n nodes have been added

double* randomLocation(): returns a random location on the surface of the sphere

vector<SpatialVertex*> findMNearestNeighbors(SpatialVertex* start): finds the m spatially nearest neighbors to some starting node

void equalize(): apply a relaxation algorithm to attempt to approximately equalize the distances between nodes by simulating repulsive forces between them